## Slide 1: Chapter 2: the image, its representation and properties
Image processing, analysis and machine vision
Dong Sun Park
Sunday, March 29, 2020

## Slide 2
Image representation and a few concepts
Image digitization
Digital image properties
Color images
Cameras: an overview
Outline

## Slide 3
Real world is continuous:
  Two v. co-ordinates in a plane.
  Three variables: is time.
2D image is the result of a perspective projection of the 3D scene
What is an image?
The continuous
Image function

## Slide 4
U =xf /z, v= yf/z
Depth recovery from 2D static images
Image function for a region R
  R = {(x,y), 1 < x<xm, 1<y<ym}
Illumination for monochromatic images
  Gray levels from black to white
Resolutions
  Spatial: proximity of samples
  Spectral: bandwidth of light frequencies captured by the sensor
  Radiometric: number of distinguishable gray levels
  Time: interval between time samples
Image function

## Slide 5
Image digitization means that the function of two-coordinates into a matrix with rows and rows.
Quantization: assigns to each continuous sample an integer value. The transition between continuous values of the image function (brightness) and its digital equivalent is called quantization.
Image digitization

## Slide 6
The number of quantization levels should be high enough to permit human perception of fine shading details in the image.
, eight bit per pixel per channel are commonly used.
Levels:
(a) 256
(b) 64
(c) 16
(d) 2

## Slide 7
Distance in image
  Euclidean
  City block
  Chessboard
Pixel adjacency: 4 or 8
Digital image properties

## Slide 8
Contiguous: if there is a path between two pixels in the set of pixels in the image, these pixels are called contiguous.
Background, object.
Region and lines.

## Slide 9
Distance transform: provides the distance of pixels from some image subset (perhaps describing objects or some features).

## Slide 11
Four distances used often in distance transform calculations

## Slide 12
Edge is a further important concept used in image analysis. The edge tells us hot fast the image intensity varies in a small neighborhood of a pixel.
Crack edge creates a structure between pixels in similar manner to that of cellular complexes.

## Slide 13
A border of a region is another important concept in image analysis.
The border of a region R is the set of pixels within the region that have one or more neighbor outside R.
Inner border or outer border.

## Slide 14
The shape of a region can be qualitatively described using the property of being convex.
A convex hull is a concept used to describe qualitative properties of objects. The convex hull is the smallest convex region containing the input region, possibly non-convex.

## Slide 15
Histograms provides a natural bridge between images and a probabilistic description.
The brightness histogram of an image provides the frequency of the brightness value in the image.

## Slide 16
Entropy: if a probability density is known then image information content can be estimated regardless of its interpretation using entropy.
An intuitive understanding of information entropy relates to the amount of uncertainty about an event associated with a given probability distribution.

## Slide 17
Visual perception of the image:
  1 Contrast: the local image change in brightness and is defined as the ratio between average brightness of an object and the background.
  2 Acuity: the ability to detect details in an image. The human eye is less sensitive to slow and fast changes in brightness in the image plane but is more sensitive to intermediate changes. Acuity also decreases with increasing distance from the optical axis.

## Slide 18
  3 Some visual illusions

## Slide 19
4 perceptual grouping is a principle used in computer vision to aggregate elements provided by low-level operations such as edges, which are small blobs to bigger chunks having some meaning.

## Slide 20
Image quality: an image might be degraded during capture, transmission or processing, and measures of image quality can be used to assess the degree of degradation.
The quality required naturally depends on the purpose for which an image is used.
Methods can be grouped into two categories:
  Subjective
  Objective

## Slide 21
Noise in image: real image are often degraded by some random errors, this degradation is usually called noise.
  White noise
  One special of white noise is gaussian noise

## Slide 22
The electromagnetic spectrum, only a narrow section is visible to a human.
Color images
Only 380-740nm

## Slide 23
Why do we see the world in color?
Two mechanisms:
  Surface reflection
  Body reflection

## Slide 24
Color perceived by human
Color sensitive receptors on the human eye are the cones.
Cones S, M, L are occasionally called B, G, and R receptively.

## Slide 25
XYZ color model space shows all colors perceivable by humans.

## Slide 26
CIE chromaticity becomes three dimensions into two dimensions.

## Slide 27
Different CIE for various field.

## Slide 28
From XYZ to RGB color space.

## Slide 29
HSV color model: Hue, saturation and value. It is often used by painters because it is closer to their thinking and technique.
Decouple intensity information from color, while hue and saturation correspond to human perception.

## Slide 30
Several color spaces and models and its applications

## Slide 31
Palette images provide a simple way to reduce the amount of data needed to represent an image. The pixel values constitute a link to a lookup table. The lookup table contains as many entries as the range of possible values in the pixel, which is typically 8 bits (256 values)

## Slide 32
Color constancy. Human vision system is able to abstract to a certain degree from the illumination changes and perceive several instances of a particular color as same. This phenomenon is called color constancy.

## Slide 33
Photosensitive sensors
  Based on photo-emission principles: explore the photoelectric effect
  Based on photovoltaic principle: is explored in several technological elements as a photodiode, and avalanche photodiode, a photoresistor, and Schottky photodiode.
  Two types of semiconductor photoresistive sensors used widely in cameras”
    CCDs, charge-coupled devices: every pixel’s charge is transferred through just one output node to be converted to voltage, buffered and sent off-chip as an analog signal. All of the pixel area can be devoted to light capture.
    CMOS: complementary metal oxide semiconductor
Camera: an overview

## Slide 34
A monochromatic camera consists of the optical system (lens), the photosensitive sensor and electronics which enables the processing of a captured image, and transfer to futher processing.
Analog
Digital

## Slide 35
Analog
Digital
Analog vs. Digital

## Slide 36
A color camera
Three strategies:
  Record three different images in succession. This is used only in precise laboratory measurements.
  Using a color filter array on a single sensor.
  The incoming light is split into several color channels using a prism-like device.